## Slide 1
WDN …
Subtitle goes here
Continues if neccessary
Author names
Address, Department of Electronic Systems, Aalborg University, Denmark
Conclusions
Emphasize what is the main contribution of your work and it’s originality
References
TBD
Introduction and System Abstraction
Modelling approach (methods)
Discussion
May be some text in bullet form:
Disturbance estimation with Kalman filter (For feed-forward?)
Package loss simulation (sensitivity to packet losses)
Cascaded control!!!!!!! (slow and fast dynamics are separated)
Linearisation
Synchronisation between Kalman and LQR
Padé approximation influence on inner loop
Leakage detection limitations (leakage has to be sudden and large)
Diagonalized system when linearised but not so much in realitiy
Results
Controller and filter design
- Outer loop tank pressure control implemented with LQR with integral action
Inner loop pump controllers made with the Root Locus design method.
Linearized transfer matrix indicated low coupling between pumps
Plot of transfer matrix
- Four second time delay modelled with second order padé approximation
FFT of consumer data used to create model of consumption pattern for Kalman Filter
Estimated consumer flow is fed forward to LQR controller
- Interaction between (stiff) Kalman filter and slow LQR controller resulted oscillations:
- Plot of Kalman-LQR oscillations
Problem formulation
How can a reliable networked controller for the WDN be
implemented that delivers constant pressure control?
Motivation
A reliable Water Distribution Network (WDN) is a pivotal part of any developed society. The objective of this project is, firstly, to both optimize the WDN control resulting in improvement in consumer experience and decreased strain on WDN components. Secondly leakage detection is introduced.
- Modeling of network was based on graph theory.
Slow and fast dynamics are separated for cascaded control
  Slow dynamics from tank dynamics
  Fast dynamics from pipe inertia
  valves, pumps and pipes includes static resistances
Model is non-linear.
  Linearised with Taylor expansion
Leakage detection and disturbance estimation with Kalman filter.
  Consumer flow is not realisticly measured
  Stiff kalman filter allows for leakage detection
  Input is based on mass conservation – what comes in and must come out
Inner Loop LQR control: The LQR controller follows constant tank pressure difference, starting 15 mm below reference.
Outer loop Pump control:
After 4h system leakage is simulated. After 8h 50% packet loss is introduced in outer loop
Consumer flow (disturbance) estimation: The Kalman filter tracking based on model and measurement data
Leakage detection: The big difference between the measured consumer flow and the Kalman Filter esitmate indicates a leakage
- Insert Kalman filter and LQR controller oscillations from incorrect tuning